## Slide 1
Roaming Arduino-Bot
Using IR LED’s and IR Sensors

## Slide 2
What It Does
Pulses IR LEDs at specific frequency
Detects reflected IR light with sensors
Drives servos forward or backward depending on sensor input logic
Effectively roams and avoids obstacles

## Slide 3: Key Components
2 Continuous Rotation Servos
2 IR LEDs
2 IR Sensors

## Slide 4
LED and Sensor Function
No obstacle detected
Obstacle detected

## Slide 5
Code
The tone() function generates a square wave of the specified frequency on a pin.
The IR sensor input signal is read and stored in a bool.
This logic value passed to the indicator LED.
The noTone() function stops the square wave generation so that tone() can be used on the other LED pin.

## Slide 6
Code
No obstacle detected:
Move both servos forward.
Right sensor detects object:
Turn left.
Left sensor detects object:
Turn right.
Both sensors detect object:
Move both servos backward.

## Slide 7
Troubleshooting
Servos drain battery FAST.
Delay() 2 ms after moving servos when obstacle encountered
Ambient light can trigger IR sensors. Dim room works best.